## Slide 1: PCB Design Flow & backup files --HSCD

## Slide 2: Design Flow
Prepare
EE provide materials ( including SCH, Rule, Stack-up, guideline and so on)
ME provide materials ( including DXF and emn ……)
Design In
Board Define and Lib path setup
All Decal/Part Type OK？
Yes
No
Create Decal /Part Type
Placement
Remind: Height limitation and Part balance
EE provide Placement and Routing Plan，specially：Power，RF，Analog signal and hi-speed signal Placement
Reference routing plan to preferentially finish critical signal or area
RD/PSE check Placement
Yes
No
Pads translate to Allegro
Setup rule
Modify Placement
Routing
Refer to “PADS to Allegro SOP”, make sure Allegro symbols are all ready.
Clean up trace, DRC/power check,
constrain setup，add testpoints
RD check Routing
Yes
No
Equal Length
DRC & Power check
Modify Routing
Backup all equal length report to others folder

## Slide 3
Follow Gerber out checklist
Refresh all symbols
OK
No
Fine tune，Trace and Silkscreen clean up
Create symbols
Next page
Must take care of height limit, component, critical trace/area when modify any issue
RD Final Check
OK
No
Modify Issues
CAM350 Check
OK
No
Modify Issues
Gerber out
Valor Check
OK
No
Release Gerber and Spec to vendor
Backup all 6 files to SVN and Finished-project folder
Project Closed
Create Testpoint Version
Add testpoint/clean up trace
Expert Check or ATE analysis
Follow CAM350 checklist
Valor check including open/short check, DRC check and power channel check

## Slide 4: Backup files
File 1: N0000-XX-XXX-cad.zip (CAD file)
File 2: N0000-XX-XXX-gerber.zip
Valor open/short report(.txt)
IPC(.ipc)
Impedance reference gerber (DIF_REF_L3.art)
panel reference gerber (T/Bsmd-ref.art)
All gerber files
File 3: N0000-XX-XXX-pads.zip (Pads PCB)
File 4: N0000-XX-XXX-smd.zip
Netlist file(.net)
SMD gerber (MASK, SMD, PLACE, SILK, X_Y)
SMD-REF DES PDF file(.pdf)
SMD-Value PDF file(.pdf)
File 5: N0000-XX-XXX-spc.zip
PCB制作要求
SMD-REF DES PDF file(.pdf)
Notation
File 6: N0000-XX-XXX-v166-brd.zip
Allegro board file
EE & ME materials & Panel
Guideline and stack up
EQL report and others